## Slide 1: Subnetting/Supernetting and Classless Addressing

## Slide 2: CONTENTS
SUBNETTING
SUPERNETTING
CLASSLESS ADDRSSING

## Slide 3
SUBNETTING
5.1

## Slide 4: IP addresses are designed with two levels of hierarchy.

## Slide 5: A network with two levels of hierarchy (not subnetted)
Figure 5-1

## Slide 6: A network with three levels of hierarchy (subnetted)
Figure 5-2

## Slide 7: Addresses in a network with and without subnetting
Figure 5-3

## Slide 8: Hierarchy concept in a telephone number
Figure 5-4

## Slide 9: Default mask and subnet mask
Figure 5-5

## Slide 10: Finding the Subnet Address
Given an IP address, we can find the subnet address the same way we found the network address in the previous chapter.
We apply the mask to the address. We can do this in two ways: straight or short-cut.

## Slide 11
Straight Method
In the straight method, we use binary notation for both the address and the mask and then apply the AND operation to find the subnet address.

## Slide 12
Example 1
What is the subnetwork address if the destination address is 200.45.34.56 and the subnet mask is 255.255.240.0?

## Slide 13: Solution
11001000 | 00101101 | 00100010 | 00111000
11111111 | 11111111 | 11110000 | 00000000
11001000 | 00101101 | 00100000 | 00000000
The subnetwork address is 200.45.32.0.

## Slide 14
Short-Cut Method
** If the byte in the mask is 255, copy the byte in the address.
** If the byte in the mask is 0, replace the byte in the address with 0.
** If the byte in the mask is neither 255 nor 0, we write the mask and the address in binary and apply the AND operation.

## Slide 15: Example 2
What is the subnetwork address if the destination address is 19.30.80.5 and the mask is 255.255.192.0?
Solution
See Figure 5.6

## Slide 16: Example 2
Figure 5-6

## Slide 17: Comparison of a default mask and a subnet mask
Figure 5-7

## Slide 18: The number of subnets must be a power of 2.

## Slide 19: Example 3
A company is granted the site address 201.70.64.0 (class C). The company needs six subnets. Design the subnets.
Solution
1s in the default
The number of mask is 24 (class C).

## Slide 20: Solution (Continued)
The company needs six subnets. This number 6 is not a power of 2. The next number that is a power of 2 is 8 (23). We need 3 more 1s in the subnet mask. The total number of 1s in the subnet mask is 27 (24  3).
The total number of 0s is 5 (32  27). The mask is

## Slide 21: Solution (Continued)
11111111 11111111 11111111 11100000
or
255.255.255.224
The number of subnets is 8.
The number of addresses in each subnet is 25 (5 is the number of 0s) or 32.
See Figure 5.8

## Slide 22: Example 3
Figure 5-8

## Slide 23: 201.70.64.000 00000-207.70.64.00011111 201.70.64.00100000-201.70.64.00111111 201.70.64.01000000-201.70.64.01011111 201.70.64.01100000-201.70.64.01111111 201.70.64.10000000-201.70.64.10011111 ; ; 201.70.64.1110000-201.70.64.11111111

## Slide 24: Example 4
A company is granted the site address
181.56.0.0 (class B). The company needs 1000 subnets. Design the subnets.
Solution
The number of 1s in the default mask is 16 (class B).

## Slide 25: Solution (Continued)
The company needs 1000 subnets. This number is not a power of 2. The next number that is a power of 2 is 1024 (210). We need 10 more 1s in the subnet mask.
The total number of 1s in the subnet mask is 26 (16  10).
The total number of 0s is 6 (32  26).

## Slide 26: Solution (Continued)
The mask is
11111111 11111111 11111111 11000000
or
255.255.255.192.
The number of subnets is 1024.
The number of addresses in each subnet is 26 (6 is the number of 0s) or 64.
See Figure 5.9

## Slide 27: Example 4
Figure 5-9

## Slide 28: Variable-length subnetting
Figure 5-10